Kirchhof’s current law (KCL)
Kirchhof’s voltage law (KVL)
DEPARTEMEN TEKNIK ELEKTRO FTUI

---
Network Topology
An interconnected set of electrical components is called a network.
Each component of a network is called
   an element.
Elements are connected by wires.

---
Nodes and Branches
The interconnections between wires are
  called nodes.
The wire paths between nodes are called
  branches.
branches
nodes

---
Nodes Connected by Wires Only
Two or more nodes connected just by
  wires can be considered as one single node.
Group of nodes connected only by wires
This network as three nodes
One big node
One big node
A single node

---
Current Flow
Current can flow through the branches of a network.
The direction of current flow is indicated by an arrow.
Note: The voltage sources in the network drive the flow
  of current through its branches.
+
_

---
Every Current has a Value and a Direction
The direction is defined by the person drawing the network.
The value is determined by the properties of the circuit.
Example:
The arrow above defines “positive” current flow i1 as downward in branch A.
Suppose that 4 mA of current flows physically downward in branch A. Then i1 = 4 mA.
Converse:
Suppose that 4 mA of current flows physically upward in branch A. Then i1 = – 4 mA.
+
_
A
 i1
_
+

---
Kirchhoff’s Current Law
The sum of currents flowing into a node
  must be balanced by the sum of currents
  flowing out of the node.
i1 flows into the node
i2 flows out of the node
i3 flows out of the node
i1 = i2 + i3
(1.2)
i1
i2
i3
node
Gustav Kirchoff was an 18th century German mathematician

---
Kirchhoff’s Current Law:
    i1 = i2 + i3
This equation can also be written in the following form:
i1 – i2 – i3 = 0
node
A formal statement of Kirchhoff’s Current Law:
 The sum of all the currents entering a node is zero.
(i2 and i3 leave the node, hence currents –i2 and –i3 enter the node.)
i1
i2
i3

---
Example 1: Kirchhoff’s Current Law:
Q: How much is the current Io ?
A: io = 2.5 mA + 4 mA = 6.5 mA
2.5 mA
io
  Similarly, i3 = 4 mA.
From KCL, i4 = i2 + i3 = 6.5 mA, and Io = i4
4 mA
i4
i2
i3
The dotted circle is a node with 2.5 mA entering
Hence i2 = 2.5 mA exits the “node”.

---
Example 2: Kirchhoff’s Current Law:
Q: How much are the currents i1 and i2 ?
A:	i2 = 10 mA – 3 mA = 7 mA
i1 = 10 mA + 4 mA = 14 mA
+
_
i1
4 mA
i2
10 mA
3 mA
4 mA + 3 mA + 7 mA = 14 mA
node

---
Sometimes Kirchhoff’s Current Law is abbreviated just by
KCL
Review: Different ways to state KCL:
The sum of all currents entering a node must be zero.
The net current entering a node must be zero.
Whatever flows into a node must come out.
more to follow…

---
General View of Networks
A network is an interconnection of elements via nodes and branches
There are many kinds of networks:
Elements	Network Connection Paths
Electrical components
Circuit
Wires
Fiber Optics
Internet
Computers
Circulatory
System
Blood Vessels
Organs
Kirchoff’s Current Law applies to all these kinds of networks!

---
Kirchhoff’s Current Law applies to all types of networks
Fiber optic network (I is light intensity)
I1
I1
I2
“KCL” for light:
I1 = I2 + I3
I3

---
Kirchhoff’s Current Law applies to all types of networks
Human Blood Vessels (f is blood flow rate)
f2
f1
f1
“KCL” for blood flow:
f1 = f2 + f3
f3
Organ

---
Voltage
Voltages are measured across the branches of a network,
 from one node to another.
The direction of a voltage is indicated by + and – signs.
+ v2 –
+
v1
 –
+
v3
 –
+
v4
 –
Remember: The voltage sources in the network
  drive the flow of current through the branches.
+
_

---
Every Voltage has a Value and a Polarity
The polarity is defined by the person drawing the network.
The value is determined by the properties of the circuit.
Example:
The plus and minus signs above define the polarity of v3 as “positive” from node 1 to node 2.
Suppose that +5 V appears physically from node 1 to node 2 . Then v3 = 5 V.
Converse:
Suppose that +5 V appears physically from node 2 to node 1 . Then v3 = –5 V.
+
_
_
+
+
v3
 –
1
2

---
Kirchhoff’s Voltage Law
The voltage measured between any two nodes
does not depend of the path taken.
v1= v2 + v3
Example of KVL:
v1= v2 + v4
Similarly:
v3= v4
and:
+
_
+ v2 –
+
v3
 –
+
v4
 –
+
v1
 –
voltage
voltage
voltage

---
Kirchhoff’s Voltage Law:
    v1 = v2 + v3
(1.3)
This equation can also be written in the following form:
 –v1 + v2 + v3 = 0
A formal statement of Kirchhoff’s Voltage Law:
 The sum of voltages around a closed loop is zero.
+
_
+ v2 –
+
v3
 –
+
v4
 –
+
v1
 –

---
Using the Formal Definition of KVL
 “The sum of voltages around a closed loop is zero.”
Define an arrow direction around a closed loop.
Sum the voltages as the are encountered in going around the loop.
If the arrow first encounters a plus sign, enter that voltage with a
(+) into the KVL equation.
If the arrow first encounters a minus sign, enter that voltage with a
(–) into the KVL equation.
For the arrow shown above:
 –v1 + v2 + v3 = 0
 –v4 – v2 + v1 = 0
For the outer arrow:
+
_
+ v2 –
+
v3
 –
+
v4
 –
+
v1
 –

---
Example 1: Kirchhoff’s Voltage Law:
Q: How much is the voltage Vo ?
A: Vo = 3.1 V + 6.8 V
A: v4 = 6.8 V
Vo
_
+
+ 3.1V –
+
 6.8 V
–
Q: How much is the voltage v4 ?
+
v4
_

---
Example 2: Kirchhoff’s Voltage Law:
Q: If v1 = 10 V and v5 = 2 V, what are v2, v3, and v4?
A:	v2 = 10 V
v3 = 10 V – 2 V = 8 V
        v4 = 2 V
+
_
        +
v1 = 10 V
        –
+
v2
–
+
v4
–
+
v5= 2 V
–
+ v3 –

---
Hitunglah banyaknya cabang dan node pada rangkaian ini. Jika Ix = 3 A dan sumber 18 V mengalirkan arus sebesar 8 A berapakah nilai RA dan Vx
Carilah Vx dan Ix

---
SOAL
Carilah X dan Y jika sumber 5 A menyuplai daya sebesar 100 W dan sumber 40 V menyuplai daya 500 W